Ter caSimulation 2
Quarter Car Model

Student: Andres F. Hoyos

Consider a two-mass quarter model with the following attributes:
Ks=100 lbs/in
Kt=1000 lbs/in
Ws=1000 lbs
Wu=100 lbs
Ct=0.01 lbs-sec/in
### Part 1: Linear Analysis
Determine the optimal suspension damping parameter using frequency response methods and human sensitivity to vibrations. Construct a time domain simulation of the two-mass quarter car model and validate the choice of suspension damping parameter with results of the frequency analysis.
Consider inputs consisting of:
1.) A one inch step function beginning at t=1s.
2.) A ¼ inch step function beginning at t=1s.
3.) A +/- 1 inch sine wave input at 1 Hz.
4.) A +/- ¼ inch sine wave at 10 Hz.
5.) A 2 inch pothole 3 ft wide at 50 mph.

Figure 1: Quarter car model diagram.

The equations of motion for the quarter car model are:

ẍ_s = - (K_s over m_s) * x_s - (C_s over m_s) * ẋ_s + (K_s over m_s) * x_u + (C_s over m_s) * ẋ_u ,

ẍ_u = (K_s over m_u) x_s + (C_s over m_u) ẋ_s + (-(K_t + K_s) over m_u) x_u + (-(C_t - C_s) over m_u) ẋ_u + (K_t over m_u) x_{"in"} + (C_t over m_u) ẋ_{"in"} .

The linear system can be expressed in state-space form:

left [ matrix { dot x_s ## ddot x_s ## dot x_u ## ddot x_u } right ] = left [ matrix { 0 # 1 # 0 # 0 ## -K_s over m_s # -C_s over m_s # K_s over m_s # C_s over m_s ## 0 # 0 # 0 # 1 ## K_s over m_u # C_s over m_u # -(K_s + K_t) over m_u # -(C_s + C_t) over m_u } right ] cdot left [ matrix { x_s ## dot x_s ## x_u ## dot x_u } right ] + left [ matrix { 0 # 0 ## 0 # 0 ## 0 # 0 ## K_t over m_u # C_t over m_u } right ] cdot left [ matrix { x_{"in"} ## dot x_{"in"} } right ]

The C matrix will determine which output is required from the system.

Determining the optimal suspension damping coefficient: